## Slide 1: WORKSHOP ON ARDUINO
BY : Abhinav
8434928102
abhinav33303@gmail.com

## Slide 2: HISTORY OF ARDUINO

## Slide 3: INITIAL HISTORY
Was a project in 2005.
Project of some students from instute of Ivrea in Italy.
Aim : To creat a low cost hardware and software which will help kids, adults , mango people and profesionals to create their own devices.
1.

## Slide 4: Need for new device
At that time students have only 1 option for developing systems.
That was : BASIC STAMP Microcontroller.
Problem : too costly arount 50$ . (2,173₹ acording to rate exchange of 2005.)
2.

## Slide 5: Who and how
In 2003 , Hernando Barragán created the development platform Wiring as a Master's thesis project at IDII, under the supervision of Massimo Banzi and Casey Reas.
Casey Reas a co-Creator of Processing IDE .
Wiring IDE Aim : Low cost tools for creating digital projects by non-Engineers
whats inside Wiring IDE ?
lets see...................................................................................
3.

## Slide 6: who and how
wiring only works for a custom pcb made by using atmega168 microcontroller.
3.

## Slide 7: Arduino Final history
In 2005
Two new guys( Massimo Banzi, with David Mellis) made a custom hardware from Atmega8 microprocessor and added it's support to wiring IDE.
These guys named their project Arduino.
and this way arduino was created .
Core members of arduino = (members of wiring ide project)+ (member of
Arduino projects)
4.

## Slide 8: Who can use arduino ?
Licensed under a CC-BY-SA license,
it means any one can manufacture and sell these board and also make systems using Arduino and sell them.
for example : Adafruit : a company sells different sensors and arduino boards.
5.

## Slide 10
Now lets start learning

## Slide 11: Basic Electronics Components

## Slide 12: Led's
Name : Light emmiting diode
Produces light when dc voltage is applied
rating : 1.5 to 3.2v and 20 mA
we use register with led
1.

## Slide 13: Registers.
we use registers to reduce the current flow , in divider circuits etc..
we measure it in Ohms.
we use it with leds to reduce the current rush ..... lets see it in our simulator.
2.

## Slide 14: Breadboard.
used for testing circuits .
sholderless connections.
first and last 2 rows are connected vertically.
and all other holes are connected horizontally.
3.

## Slide 15: Push-button.
kind of a switch.
works as it name:
push the button - circuit on.
leave it circuit off
lets see how it works on simulator.
4.

## Slide 16
Don't worry we will learn about more components later.

## Slide 18: Let's start arduino Programng

## Slide 19
Now before moving further
let's Understand Arduino Uno

## Slide 20: Arduino Uno
Arduino Uno is a one of the arduino board
Pins : digital I/O pins : 14
Analog input pins : 6
working voltage : max 5v & 500mA through usb
12v & 2A through dc jack
and 5v 1A through Vin pin.
2.

## Slide 21
Lets learn about all the pins of arduino

## Slide 22
Pin Configration in Arduino

## Slide 23
TYPES OF PINS
Power Pins
01
Analog Pins
02
Digital Pins
03

## Slide 24
POWER PINS
1. 5v Pin
2. 3.3v Pin
3. Reset Pin
4.Ground Pin
5. Vin Pin (INPUT )
01

## Slide 25
ANALOG PINS
These pins are used for capturing analog
inputs from sensors.
6 analog pins
A4 = SDA(serial data)
A5 = SCL(serial clock)
A4 and A5 pins are used for
I2C comunications
02

## Slide 26
DIGITAL PINS
PIN 0 AND 1
Pin 0 = RX (Reciver )
Pin 1 = TX (Transmitter)
Pin (0,1) used for serial communication.
means read data from another sensor/device
NOTE :
Don't connect any output device to these pins.
03

## Slide 27
PWM PINS
6 PWM Pins (3 ,5 ,6, 9 ,10 , 11)
PWM pins are represented by '~' .
PWM = PULSE WIDTH MODULATION
In simple language change voltage between 0V to 5V
04

## Slide 28
DIGITAL PINS
Used for Digital output means for on and off
in computer language these pins have 2 states
either 0 or 1. (0 = 0V and 1 = 5V)
05

## Slide 30: Programing basics.
concept you know before starting
1. functions.
2. working of if and else conditions.
3. basics of c/c++ .
Most important :
don't forget to use semicolon ;
1.

## Slide 31: Blink the Led .
OBJECTIVE :
To turn on the led for 1 second and then turn it off for the next 1 second using arduino board.
STRATEGY:
step 1 : Make the circuit
Step 2 : Program it
(moving to simulator)
2.

## Slide 32: Other Projects
2. Led dimmer with arduino.
Objective : increase/ decrease the brightness of the led's using a knob.
3. Push button with arduino.
Objective : use 2 leds, turn green led on when button is pressed otherwise turn on red led.
4. Dc motor with arduino.
Objective : use a dc motor with arduino and controll its speed.
3.

## Slide 33: Sensors and modules

## Slide 34
LDR with ARDUINO

## Slide 35
1. What is a LDR ?
LDR is short name of Light dependent resistance . It is a kind of variable resistance whose resistance varries with intensity of light . when there is low light it resistance is very high and vise versa .
Light : 400 ohms
No light : 9,000 ohms (9 kilo ohms)
These values are aprox . values deffer from ldr to ldr

## Slide 36
2. How to connect LDR with Arduino
Let's see.............

## Slide 37
3 . why Voltage divider configration ?
We use voltage divider configration to get reference voltage . But why because theoriticaly at no light , resistance of LDR is 9000 ohms whichis too much . so we use voltage divider configration.
Describing Voltage divider law in brief :
+
Vin
-
R1
R2
+ Vout (A0)
Vout= Vin x (R1 / R1+R2)
few calcution
Vin = 5 v
R1 = 1000 ohm
R2 :
day = 400 ohms
night = 9,000 ohms

## Slide 38
Light intensitiy = High :
Vout = 5 [1000 / (1,000+400)]
= 5 (1000 / 1,400)
= 3.57 V or analog value = 728
Light intensitiy = LOW :
Vout = 5 [1,000/ (1,000+9,000)]
= 5 (1,000/ 10,000)
= 0.5 V or analog value = 102
Vout = R1
___________
R1+R2
( )
Vin

## Slide 39
Lets do programming.........

## Slide 40
SERVO MOTORS

## Slide 41
WHAT IS A SERVO MOTOR
It is a type of motor whose motion can be controlled in terms of angle . for example 15 degrees ,90 degrees etc.

## Slide 42
Types of servo motors
There are manly 2 type of servo motors
1. 180 degree servo motors
2. 360 degree / continous servo motors

## Slide 43
Different sizes of servo motors

## Slide 44
How to interface Servo motors with arduino
Pin configration of servo motor

## Slide 45
Now lets learn its programming

## Slide 46
Ultrasonic Sensor

## Slide 47: How Ultrasonic sensors work ?
Sends a high frequency sound (ultrasound) and wait for sound to reflect back.
count how much time it takes to come back .(we can call this echo )
speed = distance /time . so,
Time = distance / speed

## Slide 48
Speed of ultrasound = 340 m/s
or 0.034 cm / micro sec
lets say object is at 1 cm away so
distance = 2cm (because ultrasound will cover twice the distance )
time = 2/ 0.034 = 58.8 micro sec.

## Slide 49: microcontrollers calculation.

## Slide 50: Our sensor HC- SR04
HC-SR04 Specifications
Working Voltage: DC 5V
Working Current: 15mA
Working Frequency: 40Hz
Max Range: 4m
Min Range: 2cm
Measuring Angle: 15 degree

## Slide 51: Projects :
Digital scale
Parking sensor
Blind stick
I.O.T projects .....like distance avoiding bot , water level indicators etc...

## Slide 52: Pin configration :
Vcc : +5 v
Trig : Transmitter pin(Output pin)
Echo : Reciever pin (Input pin)
Gnd : Ground pin

## Slide 53: Circuit Digram
lets see ....